Model: LulzBot Bio Printer

  Serial Number:
  Date Completed:
  Tested by:

Configuration:

  Electronics:	EinsyRetro 1.0a
  Firmware:	Marlin Version

Motor Axis	Steps/mm	Travel	Microstep Mode	Digipot
X	100	160 mm	16 μsteps/step	920 mA
Y	100	160 mm	16 μsteps/step	920 mA
Z	200	180 mm	32 μsteps/step	960 mA
E0	9448.8	NA	16 μsteps/step	960 mA

General:
- Are all the screws torqued to spec?
- Are all the zip ties tight?
- Are the switches and bump stops installed securely?
- Are all 4 rubber feet installed?
- Is the frame free of scratches and scuffs?
- Is the certification sticker free of bubbles, debris, and straight?
- Wipe down the frame so it is free of dust and schufs.

Y Axis:
- Does the Y bed move freely back and forth?
- Is the Y bed tight side to side from motion and twisting?
- Is the Y belt free from rubbing on the y-idler by the bearings?
- Are the Y pulley set screws tight with one aligned with the flat on the motor shaft?
- Is the Y belt tightened to spec?
- Are the four bed leveling washers tight?
- Are the belts trimmed far enough to not interfere with the pulley or bearing?

X Axis:
- Are the X pulley set screws tight with one aligned with the flat on the motor shaft?
- Is the X belt free from rubbing on the x-idler by the bearings?
- Is the X belt tightened to spec?
- Does the X axis move freely end to end?
- Are the wires and zip ties behind the carriage free from touching the case wall?

Z Axis:
- Are the Z belts tensioned within spec?
- Are the compression bushing set according to the instructions in the OHAI?
- Are the belts aligned, and do they not rub?
- Are the belt ends secured in the tensioning collar, with no interference with the axis travel?
- Are the Z-Belt tension collars pushed flush to the printed part?
- Are the pulley set screws tight?

Electronics:
- Are all connections to the Einsy plugged in correctly?
- Are all cables free from contacting any moving parts?
- Has the protective plastic been removed from the LCD?
- Has the protective cover been removed from the clear polycarbonate LCD cover?
- Does the LCD not move up or down or side to side?
- Did the printer pass Hi-Pot Testing?

Test and Verification Results:
- Verify LCD functions normally.
- Belts aligned on bearings and properly tensioned.
- Verify case fan is running.
- Syringe Pump control verified.
- Verify machine can be auto-homed 5x without issues.
- Verify that both carriages touch the Z-motor mounts during the start up leveling routine.
- X,Y, Z motion smooth over range and speeds.
- Threadlocker applied to all pulley set screws.
- Re-check all belt tensions.
- Syringe Pump moved to shipping position.